## Slide 1: LED Matrix Timer
…and other things
Krisztián Stancz 30.06.2017

## Slide 2: We’ll discuss…
Introduction to LEDs
Driving LEDs
Multiplexing and Charlieplexing
Using shift registers
A look into the code
Having more than 4 colors
LED matrix prices

## Slide 3: LED basics

## Slide 4: Basic LED circuit
Anode
Cathode
Cathode
Anode
R = UR / IR
R = (UPowerSupply - ULED) / ILED

## Slide 5: How to find ULED and ILED

## Slide 6
R = (UPowerSupply-UF) / IF
R = (5V – 1.8V) / 20 mA
R = 160 ohm

## Slide 7: Driving LEDs with an MCU
Output
5V
DDRD |= (1 << DDRD0);
PORTD |= (1 << PORTD0);

## Slide 8: Driving LEDs with an MCU
Output
0V
DDRD |= (1 << DDRD0);
PORTD &= ~(1 << PORTD0);

## Slide 9: Driving LEDs with an MCU
DDRD |= (1 << DDRD0);
while (1) {
PIND |= (1 << PIND0);
_ms_delay(500);
}

## Slide 10: Confusing detour
current
flow
Output
5V
DDRD |= (1 << DDRD0);
PORTD |= (1 << PORTD0);

## Slide 11: Confusing detour
current
flow
Output
0 V
DDRD |= (1 << DDRD0);
PORTD &= ~(1 << PORTD0);
WTF???

## Slide 12: Confusing detour

## Slide 13: Confusing detour
Output = Control the environment
Input = Observe the environment
Work with voltages

## Slide 14: Tri-state pins

## Slide 15: Multiplexing vs Charlieplexing
C1
2 pins
2 pins

## Slide 16: Multiplexing vs Charlieplexing
C1 C2
5 pins
3 pins
Output 0V
Output 5V
Output 0V
Output 5V
Output 0V
Input High Impedance
Output 0V
Output 5V
(N2 – N) LEDs
(N2 / 4) LEDs
for N pins:

## Slide 17: 8x8 LED matrix
64 LEDs
16 pins

## Slide 18: 8x8 LED matrix
Common anode
Common cathode
5V
5V
5V
5V
0V
5V
5V
5V
0V
0V
0V
0V
5V
0V
0V
0V
0V 0V 0V 5V 0V 0V 0V 0V
5V 5V 5V 0V 5V 5V 5V 5V

## Slide 19: 8x8 LED matrix
Common anode
Common cathode
0V
0V
0V
0V
0V
0V
0V
0V
0V
0V
0V
0V
5V
0V
0V
0V
0V 0V 0V 5V 0V 0V 0V 0V
0V 0V 0V 0V 0V 0V 0V 0V

## Slide 20: 8x8 RGB LED matrix (common cathode)
192 LEDs
32 pins

## Slide 21: Shif register (74HC595N)
MCU

## Slide 22: Shifting out

## Slide 23: Daisy chaining shift registers
Clock
Latch
Serial data in when latch low
Parallel data out when latch high
Serial data overflow
Clock
Latch
Serial data in when latch low
Serial data overflow
Parallel data out when latch high
To next IC
From MCU
data pin

## Slide 24: Putting it together

## Slide 25: In reality

## Slide 26: Writing on a LED matrix
For loops
Bitmaps
  RGB+Column: 32 bytes
  8 x 4 = 32 bytes per bitmap
  Memory for variables: 1024 Bytes -> 32 bitmaps
  Program memory
    16 kBytes
    PROGMEM macro
In-between

## Slide 27: Writing on a LED matrix

## Slide 28: Button and timer

## Slide 29: 16 777 216 colors?
Using 8 bit timer PWM
RGB: 256 x 256 x 256 colors
In theory only
Human perception:
  Non-linear brightness sensing
  5% - 1 % > 99% - 95%
Refresh frequency

## Slide 30: Price range on Ebay

## Slide 31: Flexible, addressable LED matrix

## Slide 32: Full code available:
https://github.com/skrisztian/led-matrix-timer